| >>>Computer Numerically Controlled<<< |
| --- |
| Tasks: |
| Program machining of work piece with G90 and for centre point path of the tool! Use commands G0 and G1! Enter program %2 into your computer and simulate machining! Consult your teacher for removing of any errors! |
| Input: |
| Tool – change - point (WWP): X=150; Y=100; Z=50 Rotation speed (S): 1200 1/ min Feed rate (F): 60 mm/min Milling depth: 6 mm Tool: T1 cutter Ø10 | M03 spindle ON, clockwise rotation M30 main program STOP G00 fast movement (rapid feed) G01 straight line with given feed G90 absolute position |

# Text boxes

#### Zespo( Szkó( Mechanicznych

w Bia(ystoku